## Slide 1
Team Lead Name
MOULESH S
Team Members
RAGURAMAN J
ANANTH KUMAR A
Mentor : SANTHOSH P
College Name – University College of Engineering Villupuram
AI
AI
AI
AI
AI
AI
AI
AI
AI
AI
AI
EV BATTERY THERMAL & COOLING OPTIMIZATION
Physics + ML Hybrid Cooling Simulation

## Slide 2
Project Objectives
Problem Statement
01
Project Overview – Introduction
02
End Users
03
Wow Factors in Project
04
Modelling / Block Diagram / Flow of Project
05
Technology Stack
06
Result / Outcomes
07
Conclusion
08
Future Perspective
09

## Slide 3
Problem Statement
1. Overheating Under Load
Highway and hill-climb bursts push cell current past 10 A.
With no cooling, the core peaks at 44.2°C.
The core stays above 35°C for 58.4% of the run.
2. Reactive Cooling Lags
Bang-bang cooling waits until the surface reaches 34°C.
Core still peaks at 36.8°C and is over 35°C for 14.2% of the run.
On/off switching gives a high wear score of 14.2.
3. Cooling Costs Energy
Pump power grows with flow cubed (P ∝ u³).
Hard, late cooling is wasteful: 1.75 Wh for bang-bang.
Cooling must start early and stay just strong enough.
Project Goal: Build an interactive physics + ML simulator that compares four cooling strategies on a 21700 battery cell and finds the one that protects it with the least pump energy.

## Slide 4
Project Overview - Introduction
The EV Battery Thermal & Cooling Simulation is a browser dashboard that models a 21700 cell with a two-state thermal model and compares four cooling strategies live, including an ML look-ahead controller.
Two-state (core / surface) lumped thermal model.
Bernardi heat generation with temperature and aging effects.
Four strategies: Passive, Bang-Bang, PID and ML Look-Ahead.
Live waveforms, metrics and a 21700 cell thermal view.
Four load profiles, including NASA B0005 and fast charge.
Live benchmark table comparing all four strategies.
21700
cell format modelled
2
thermal states: core and surface
4
cooling strategies compared
4
drive-load profiles
Model at a glance

## Slide 5
End Users
EV Thermal / BMS Engineers
Compare cooling controllers before building any hardware.
Battery Researchers
Study heat generation, aging and the core-to-surface gradient.
Students & Educators
Teach thermal management and control with a live demo.
Pack & Cooling Designers
Judge pump energy against protection when sizing cooling.
One platform to model • predict • cool • save energy

## Slide 6
Wow Factors in Project
ML Look-Ahead Cooling
Forecasts core temperature 10 s ahead and pre-cools before the heat spike.
Live Strategy Switching
Switch between four controllers while the simulation keeps running.
Real-Time Waveforms
90-second strip charts of temperature, coolant flow and load current.
21700 Cell Thermal View
Core, surface and coolant ring change colour as the cell heats up.
Live Benchmark Table
Peak temperature, time over 35°C, pump energy and wear score.
What-If Controls
15 A burst pulse, ambient and coolant sliders, aging cycles, 1x-10x speed.

## Slide 7
Modelling/Block Diagram/Flow of Project
INPUT
Drive Profile
Load current I(t): city/highway, NASA B0005, fast charge, hill climb
Environment & Aging
Ambient and coolant temperature sliders, battery cycle index
Simulation & Control Engine (1 s step)
Heat Generation
Bernardi: I²R + entropic heat; Arrhenius R_int and aging
Thermal Model
Core / surface equations, C = 38 / 8 J/K
ML Forecast
Predicts core temperature 10 s ahead
Cooling Controller
Passive, Bang-Bang, PID or Look-Ahead sets flow u
OUTPUT
Live Waveforms
Temperature, flow, current
Cell Thermal View
21700 core and surface
Metrics Strip
Six live readouts
Benchmark Table
All four strategies
Delivery: single responsive web dashboard (HTML, Tailwind CSS, Canvas and SVG) that runs in any browser

## Slide 8
Technology Stack
Physics Model
Lumped 2-state thermal equations
Bernardi heat generation
Arrhenius R_int + aging factor
Euler step, dt = 1 s
Control & ML
Bang-Bang: on 34°C, off 29.5°C
PID with a 30°C target
ML look-ahead forecast, t + 10 s
Slew-limited flow command
Frontend
HTML5 and JavaScript
Tailwind CSS responsive layout
Selectors, sliders, burst button
Dark dashboard theme
Visualization
HTML5 Canvas strip charts (90 s window)
Inline SVG 21700 cell cross-section
Live status badges and metric tiles
Actuator & Energy
Pump power P = 45 W × u³
Maximum cooling transfer 2.5 W/K
Cumulative parasitic energy in Wh

## Slide 9
Result/Outcomes
LIVE DASHBOARD & METRICS
BASELINE
Passive (No Cooling)
u = 0, natural convection
REACTIVE
Hysteresis (Bang-Bang)
On at 34°C, off at 29.5°C
FEEDBACK
Closed-Loop PID
P-I-D feedback control
OPTIMAL AI
ML Look-Ahead (MPC)
Anticipatory pre-cooling
Core Temp
24.0 °C
Normal operating
Surface Temp
24.0 °C
From thermistor
Forecast +10 s
24.0 °C
Steady trend
Load Current
0.0 A
0.0 W heat gen.
Coolant Flow
0.0 %
0.0 W parasitic
Parasitic Energy
0.000 Wh
Saving vs ref.
Metric values shown are the simulation start state (24°C ambient, 0 A load).
Header controls: Run / Pause, 15 A Burst Pulse, Reset and 1x to 10x simulation speed.
Panels: live waveforms, 21700 cell view, drive-cycle parameters and the strategy benchmark.

## Slide 10
Result/Outcomes
LOAD PROFILE & LIVE WAVEFORMS
Chart: Dynamic city / highway load current I(t), two 75 s cycles
Waveform panel guide
T_core
T_surf
Forecast (t+10 s)
Target 30°C
Critical limit 35°C
Coolant flow u(t)
Load current I(t)
75 s cycle: idle, urban cruise, highway burst (up to 13 A), regenerative braking (-2.5 A), moderate cruise, coast. The burst is what drives the heat spike.

## Slide 11
Result/Outcomes
21700 CELL THERMAL STATE & DIAGNOSTICS
CORE
T_core
SURFACE T_surf
Coolant jacket (cold plate)
Core status badges
Optimal Zone
core ≤ 30.5°C
Cooling Engaged
30.5 to 35°C
Thermal Stress
core > 35°C
Cell colour scale (°C)
< 26
26-30
30-33
33-36
≥ 36
ΔT (core - surface)
0.00°C
Internal resistance R_int
45.0 mΩ
Cooling power Q_cool
0.0 W
Estimated SOC
95.0%
Diagnostic values shown are the start state.

## Slide 12
Result/Outcomes
STRATEGY BENCHMARK
Strategy | Max core | > 35°C | Energy | Saving | Wear score
Uncontrolled (Passive) | 44.2°C | 58.4% | 0.00 Wh | -- | 0.0
Hysteresis (Bang-Bang) | 36.8°C | 14.2% | 1.75 Wh | Reference | 14.2 High
Closed-Loop PID | 33.9°C | 0.0% | 0.92 Wh | +47.4% | 6.8 Med
ML Look-Ahead (MPC) | 31.8°C | 0.0% | 0.41 Wh | +76.5% | 3.2 Smooth
Chart: Max core temperature (°C)
| Passive | Bang-Bang | PID | ML Look-Ahead
Max core temperature (°C) | 44.2 | 36.8 | 33.9 | 31.8
Values as shown in the dashboard benchmark table.
Optimization insight: pre-cooling at a moderate flow rate uses the pump affinity law, P ∝ u³. It removes the heat spikes and cuts parasitic energy by over 75% compared with bang-bang cooling.

## Slide 13
Result/Outcomes
PUMP AFFINITY LAW & ENERGY SAVINGS
Chart: Pump power vs coolant flow: P = 45 W × u³
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Pump power | 0 | 0.006 | 0.045 | 0.152 | 0.36 | 0.703 | 1.215 | 1.929 | 2.88 | 4.101 | 5.625 | 7.487 | 9.72 | 12.358 | 15.435 | 18.984 | 23.04 | 27.636 | 32.805 | 38.582 | 45
50% flow | 5.625
Chart: Parasitic pump energy (Wh)
| Passive | Bang-Bang | PID | ML Look-Ahead
Parasitic pump energy (Wh) | 0 | 1.75 | 0.92 | 0.41
Takeaway: half flow needs only 12.5% of full pump power, so gentle early cooling beats late full-flow bursts.

## Slide 14
Conclusion
EV BATTERY THERMAL & COOLING OPTIMIZATION
Models a 21700 cell with a two-state thermal model and Bernardi heat generation.
Compares Passive, Bang-Bang, PID and ML Look-Ahead cooling on identical loads.
ML look-ahead holds the core at 31.8°C with no time above 35°C.
Pre-cooling cuts parasitic pump energy by 76.5% versus bang-bang.
Gives engineers and students a real-time, interactive thermal tool.
Future Goal: validate against real cell data and replace the rule-based look-ahead with a trained forecaster.

## Slide 15
Future perspective
Real Cell Validation – Fit the model to measured NASA B0005 and thermistor data.
Trained Forecaster – Replace the rule-based look-ahead with a learned model.
Pack-Level Model – Extend from one cell to a multi-cell pack and cold plate.
Hardware-in-the-Loop – Drive a real pump and BMS with the controller.
Aging-Aware Control – Adapt cooling as internal resistance grows with cycles.
Fast-Charge Limits – Tie charge-rate limits to cell temperature.
Real Data
ML Forecaster
Pack Model
HIL Testing
Aging-Aware
Fast Charge
Future Goal: a validated, pack-level thermal platform with a learned controller ready for real hardware.

## Slide 16
Thank You !!